## Slide 1: Microprocessor Systems
Prof. Ren-Shuo Liu
NTHU EE
Lab7-1 IR Distance Measuring Sensor-GP2Y0A51SK0F
& Analog Digital Convertor-MCP3202

## Slide 2: Introduction
GP2Y0A51SK0F is a distance measuring sensor unit.
Composed of an integrated combination of
  PSD (position sensitive detector)
  IR-LED (infrared emitting diode)
  Signal processing circuit

## Slide 3: Features
Short measuring cycle (16.5ms)
Distance measuring range : 2 to 15 cm
Compact size (27.0 × 10.8 × 12.0mm)
Analog output type

## Slide 4: IR Sensors Key Applications
TVs, computers, laptops
Distance measurement (in this lab)
Security systems such as surveillance, burglar alarms, etc.
Monitoring and control applications

## Slide 5: IR Sensors Key Applications

## Slide 6: Appearance
LED
PSD
An IR LED emitter lens that emits a light beam.
A position-sensible photodetector (PSD) where the reflected beam will fall onto.

## Slide 7: Block Diagram

## Slide 8: Basic Working Theory
This device outputs the voltage corresponding to the detection distance.

## Slide 9: Position Sensitive Detector

## Slide 10: Position Sensitive Detector
The two output electrodes receive different intensities, I1 and I2, which are based on the incident beam position x.
The incident beam position x can be calculated with the formula below, and further used to determine the incident light spot distance.
x=L*(I2-I1)/(I2+I1)
l2
l1

## Slide 11: Triangulation Measurement
The angle between reflective light and PSD can be derived knowing the centroid position of reflective light(X).
The distance between object and device can then be calculated by triangulation.
PSD
Angle 1
Angle 2
X2
X1

## Slide 12: Timing Chart
Measuring cycle 16.5ms
Max output delay 5ms

## Slide 13: Example of Output
X-axis: Distance to the reflective object(cm).
Y-axis: Analog voltage output(V)
Output voltage drops with greater distance.

## Slide 14: Analog Digital Converter-MCP3202
We need an ADC to convert the analog output from the IR distance sensor to digital values.
MCP3202 is a 12-bit resolution ADC

## Slide 15: ADC Introduction
4095
A/D Conversion
Sampling rate for MCP3202
  Maximum 100 ksps at VDD = 5V
  Maximum 50 ksps at VDD = 2.7V

## Slide 16: N-bit Output Code
0
A unit step is VDD/2n
2n-1
Converted Voltage= Converted Value*VDD/2n-1
In our case, n=12

## Slide 17: Block Diagram
Using SPI interface, same as MAX7219 in LAB2

## Slide 18: Timing Diagram
The first DIN with CS low consists of a start bit.
Sampling time = 1.5 cycles.
Start

## Slide 19: Work Mode
Single-ended(1)/Channel select(0 or 1)
Pseudo-Differtial(0)/Polarity(+ or -)

## Slide 20: Work Mode
MSBF bit is transmitted and used to enable the LSB-first format.
If the MSBF bit is low, the device will output the converted word LSB first after the word has been transmitted in the MSB-first format.

## Slide 21: Communicate with 8 bit MCU
Data is transmitted from ADC on falling edges of SCLK.
Data is received by MCU on rising edges of SCLK.

## Slide 22: Communicate with 8 bit MCU
1bit null+12bit ADC output
2bit choose mode+1bit MSBF
1bit start
It is required to send groups of 8 bits, how do we deal with it?
In order to get these 17 bits, we need 8*3=24cycles.

## Slide 23: 8 Bit MCU Transmission Arrangement
First byte transmitted to the A/D converter contains seven leading zeros before the start bit.
This way produces the output 12 bits to fall in positions easily manipulated by the MCU.

## Slide 24: 8 Bit MCU Transmission Arrangement
MCU receive buffer will contain three unknown bits until the null bit is clocked out.
Second byte consists of Null bit and the highest order four bits of the conversion.
Highest order four bits of the conversion

## Slide 25: 8 Bit MCU Transmission Arrangement
Third byte consists of lowest order eight bits of the conversion.
Easier manipulation of the converted data can be obtained by using this method.
lowest order eight bits of the conversion

## Slide 26: Reference
https://global.sharp/products/device/lineup/data/pdf/datasheet/gp2y0a51sk_e.pdf
https://www.researchgate.net/publication/279171564_Novel_Method_of_Detecting_Movement_of_the_Interference_Fringes_Using_One-Dimensional_PSD
https://ww1.microchip.com/downloads/en/DeviceDoc/21034F.pdf
https://en.wikipedia.org/wiki/Analog-to-digital_converter

## Slide 27: IR Sensor Operating Interval

## Slide 28: IR Sensor Measuring Interval

## Slide 29: Microprocessor Systems
Prof. Ren-Shuo Liu
NTHU EE
Lab7-2 MLX90614 IR Thermometer

## Slide 30: Introduction
MLX90614 is an Infrared thermometer for noncontact temperature measurements
MLX90614 is built with 2 chips
  Infrared thermopile detector MLX81101
  Single conditioning ASSP MLX90302

## Slide 31: Features
Measuring ambient temperature () and object temperature ()
Factory calibrated in wide temperature range
  -40°C ~ +125˚C for sensor temperature ()
  -70°C ~ +380˚C for object temperature ()
Measurement resolution of 0.02°C
Sleep mode for reduced power consumption

## Slide 32: Applications of MLX90614
Non-contact thermometer​ (Lab project)
Temperature Measurement of moving objects
Industrial Thermal Gun
Human Body Temperature Measurement
Home/Office Temperature Control
Livestock Monitoring
Movement Detection

## Slide 33: Block Diagram

## Slide 34: MLX90614

## Slide 35: MLX90614 With PCB

## Slide 36: Connection with MCU

## Slide 37: Field of View
How Field Of View For Infrared Temperature Sensors Is Determined
https://youtu.be/vpN-myfTAOs

## Slide 38: SMBus Compatible 2-wire Interface
Slave address: 0x5A

## Slide 39: Electrical Specifications
Typical Supply current = 1.3mA
Sleep mode current = 2.5uA

## Slide 40: EEPROM
Size : 32x16 bits ( 32 register , 16 bit/register )

## Slide 41: RAM
Size : 32x16 bits ( 32 register , 16 bit/register )

## Slide 42: Command
Note *: The xxxxx represent the 5 LSBits of the memory map address to be read / written
Note **: Behaves like read command. The difference is that the read flags does not have a repeated start bit
Five bits correspond to 32 registers

## Slide 43: Bit Transfer

## Slide 44: Read Word
Access RAM, read ,

## Slide 45: Write Word
Write data in EEPROM

## Slide 46: SMBus Communication Example

## Slide 47: SMBus Communication Example
Command 0x22 = 0010_0010

## Slide 48: Computation of Ambient and Object Temperatures
Thermopile output signal: (, ) = A x (x)
  Absolute object temperature
  Sensor die absolute temperature
  A: Sensitivity
, are derived from RAM
  [°C] = x 0.02 – 273.15
    0x06 = 0x2DE4 (11748d) corresponds to -38.2 °C
    0x06 = 0x4DC4 (19908d)corresponds to +125 °C
  [°C] = x 0.02 – 273.15
    0x27AD corresponds to -70 °C
    0x7FFF corresponds to 382.19 °C

## Slide 49: Reference
https://www.melexis.com/zh/documents/documentation/datasheets/datasheet-mlx90614
https://www.mouser.tw/datasheet/2/268/mic5270-1891236.pdf