## Slide 1
Microprocessor Systems
Lab10 – From 8051 to ARC
Prof. Ren-Shuo Liu
NTHU EE

## Slide 2: Digital Hourglass
Calculator
IR Thermometer
ISP Burner
POV Clock
Music Synthesizer

## Slide 3
GPIO
SPI interface
7-segment and its driver (MAX7219)
Matrix keyboard scanning
I2C and SPI interfaces
OLED and its driver (SSD1305)
IR thermal sensor (MLX90614)
IR distance sensor
ADC (MCP3002)
I2C interface
6-Axis gyroscope (MPU6050)
Matrix LED and its driver (MAX7219)
Timer

## Slide 4
AT89S51 ISP protocol
Minimal 8051 system
Assembly delay
Assembly Interrupt
Mixed C and ASM programming
Hall sensor
External interrupt
Timer
Software-based LED scanning
Audio synthesis
32-bit controller
DAC

## Slide 5: Digital Hourglass
Calculator
IR Thermometer
ISP Burner
POV Clock
Music Synthesizer

## Slide 6: Importance of the Microcontroller and Embedded System Course
邏輯設計邏設實驗
(Digital Logic Design)
C, C++, Python程式設計 (Programming)
電子學 子路實驗
(Microelectronics)
6

## Slide 7: Microcontrollers Such as 8051
CPU | RAM | ROM
I/O Port | Timer | Serial COM Port

## Slide 8: Microcontrollers vs. Common Computers
8
CPU | RAM | ROM
I/O Port | Timer | UART
Bare-Metal
User Program (C and ASM)
Operating System
User Program
(C, C++, Python, etc.)
Library, Driver
Libraries

## Slide 9
 | AT89S51 | Arduino UNO (ATMega328p) | ARC EM | Raspberry 4 (BCM2711)
Pin count | 40 | 28 |  | 
ISA | CISC | RISC | RISC | RISC
Word size | 8 | 8 | 32 | 64 (4 cores)
Frequency (Hz) | 33 M | 20 M | 400 M | 1.5 G
Program Memory | 4 K (On-chip) | 32 K (On-chip) | 2 MB | SD card
Data memory | 128 B | 2 KB | 2 MB | Up to 8 GB (off chip)
GPIO | 32 | 23 | 3 (44) | Up to 28
Timer | 2 | 3 | 2 | 5
PWM channels | 0 | 6 | 0 (6) | 4
ADC channels | 0 | 8 | 0 (16) | 
Serial | UARTx1 | USB, UART SPI, I2C | I2Cx1 (USB, UARTx4, SPIx3, I2Cx3, SDIOx2, I2S) | USB, SDIO x2 (I2C or UART) x6 SPI x5, HDMI x2

## Slide 10: Himax WE-I Plus

## Slide 11: WE-I Features
CPU: HX6537 (ARC EM9D DSP with FPU)
Frequency: 400MHz
SPI program flash: 2MB
Ram size: 2MB 320kB program ICCM
320kB data DCCM/XCCM/YCCM 1472kB system memory

## Slide 12: WE-I Features
UART: 1 (for USB VCP)
SPI: 1 (for USB VCP)
I2C Master: 2 (1 for IMU, 1 for user use)
GPIO: 3

## Slide 13: WE-I Features
CPU HX6537
HM0360 AoSTM VGA camera Back Side Illuminated (BSI) CMOS Image Sensor
Active Pixel Array: 656 x 496 Frame Rate: QQVGA 1FPS to VGA 60FPS
Reset Button

## Slide 14: WE-I Features
4. LSM9DS1 IMU sensor
3 acceleration: ±2 / ±4 / ±8 / ±16 g
3 angular rate : ±245 / ±500 /
±2000 dps
3 magnetic field: ±4 / ±8 / ±12 /
±16 gauss
16-bit data output
5. Green & red LED

## Slide 15: WE-I Features
15
6. Header 7*1 pitch=2.54 Pin1: 3V3
Pin2: GPIO0 Pin3: GPIO1 Pin4: GPIO2
Pin5: I2C_M1_SCL Pin6: I2C_M1_SDA Pin7: GND
7. Microphones (L/R) at back side

## Slide 16: Comparison
 | 8051 Development Board | WE-I
Processor | AT89S51 | EM9D Core
 | 8-bit | FPU
Supply Voltage (V) | 5 | 3.3
Clock Frequency (MHz) | 0 ~ 33 | 400
Memory (Byte) | FLASH: 4K | FLASH:
 | SRAM: 128 | SRAM: 2M
UART | X 1 | X 1
SPI | none (created by firmware) | 1
I2C | none (created by firmware) | 2 master

## Slide 17: Lab10 on Next Tuesday- Ping Pong Test
Ping Pong
Start Point
Rebound after hitting boundary

## Slide 18: Lab on Next Tuesday- Ping Pong Test
We will compare the speed of the program between WE-I and 8051 next Tuesday
WE-I vs 8051
Which one is faster?

## Slide 19: Lab10 Example Project Procedure
Start
Initialize Peripheral Module Calculate Ball Position
Update OLED Screen
Firmware Create I2C Protocol
firmware finish
I2C Peripheral Module
I2C module finish
WE-I
8051

## Slide 20: Main Difference
 | 8051 | WE-I
Core | AT89S51 | EM9D
I2C | Firmware | Peripheral Module
Calculating | Emulated FP | FPU

## Slide 21: Microprocessor Systems
Embedded Operating System
Prof. Ren-Shuo Liu
NTHU EE

## Slide 22: Outline
Operating System (OS)
Bare-metal / Bare-machine
  Super-loop programming style
Key concepts
  Concurrent tasks (threads)
  Time multiplexing
  Preemption
  User mode vs. kernel mode
  Real-time OS (RTOS)
  Mutex and semaphore

## Slide 23: Operating Systems
Software that manages hardware resources to run other software on the hardware
Examples
  Windows XP, Windows 7, Windows 8 …
  Linux, including the Ubuntu, Fedora, CentOS… distros
  Android
  iOS
Those specifically for embedded systems
  TinyOS, FreeRTOS, RTLinux, Zephyr…

## Slide 24: Q: Which are OSes
Keil
Python
GCC
Arduino
Dos
Microsoft
TensorFlow

## Slide 25: Bare-metal (Bare-machine)
Developing and directly running software on hardware that has no OS
Benefits
  Each function owns the entire CPU and occupies interfaces (e.g., UART)
Drawbacks
  Difficult to implement a system that concurrently do multiple functions
  Waste CPU time for slow

## Slide 26: Example
keyboard scanning and de-bouncing + OLED displaying
  Keyboard may becomes less unresponsive when the microcontroller is drawing the OLED
Things become complicated if we want more tasks to do in parallel, e.g.,
  UART communication
  6-axis sensing
  ADC
  …

## Slide 27: Super Loop
Super loop is a naïve (and also useful) programming style for bare-metal programming
Start
Initialization
Keyboard
OLED
UART
Delay (optional)
int time = 0;
int main()
{
...
for(;;){
keyboard();
OLED();
UART();
delay(10);
time++;
}
return 0;
}
void keyboard()
{
if(time%10==0){ //100 ms
keyAction();
}
return;
}
void OLED()
{
if(time%5==0){ //50 ms
oledAction();
}
return;
}

## Slide 28: Concurrent Tasks
What if we have multiple CPUs
void keyboard()
{
while(1){
keyAction();
delay(100); //100 ms
}
return;
}
void OLED()
{
while(1){
oledAction();
delay(50); //50 ms
}
return;
}
int main()
{
...
taskCreate(keyboard);
taskCreate(OLED);
taskCrate(UART);
taskStart();
while(1);
}
Start
Initialization
Keyboard
OLED
UART

## Slide 29: Concurrent Tasks
What if we have multiple cores to concurrently do multiple tasks
Start
Initialization
Keyboard
OLED
UART
void keyboard()
{
while(1){
keyAction();
delay(100); //100 ms
}
return;
}
void OLED()
{
while(1){
oledAction();
delay(50); //50 ms
}
return;
}
int main()
{
initialization()
startCore(1, keyboard);
startCore(2, OLED);
startCore(3, UART);
while(1);
}

## Slide 30: Time Multiplexing
OS can virtualize a core into multiple cores by using time multiplexing (i.e. time sharing)
Start
Initialization
Keyboard
OLED
UART
void keyboard()
{
while(1){
keyAction();
sleep(100); //100 ms
}
return;
}
void OLED()
{
while(1){
oledAction();
sleep(50); //50 ms
}
return;
}
int main()
{
...
taskCreate(keyboard);
taskCreate(OLED);
taskCrate(UART);
taskStartScheduler();
while(1);
}
Task Scheduler
All interrupts, including timer,
or sleep
Schedule

## Slide 31: Pre-emptive vs. Non-preemptive OS
Preemption: 搶佔
Preemptive OS has the right to suspend tasks
  For time sharing (timer interrupt)
  For prioritizing other tasks (e.g., external interrupt)
In a non-preemptive OS, a task can occupy CPUs as long as it wishes
  OS does not force tasks to relinquish the CPU
  Tasks have to co-operate by themselves
    This is not the case for Windows, Linux, Android. Otherwise, a buggy user program can occupy the computer

## Slide 32: Preemptive Fixed Priority Scheduling
High Priority Task
Low Priority Task
Time
Example from Prof. Brad Campbell

## Slide 33: Preemptive Fixed Priority Scheduling
High Priority Task
Low Priority Task
Time

## Slide 34: Preemptive Fixed Priority Scheduling
High & low priority jobs arrived together
High & low priority jobs arrived together
High Priority Task
Low Priority Task
Time

## Slide 35: Preemptive Fixed Priority Scheduling
High priority job is executed first
High Priority Task
Low Priority Task
Time

## Slide 36: Preemptive Fixed Priority Scheduling
Low priority job is executed later
High Priority Task
Low Priority Task
Time

## Slide 37: Preemptive Fixed Priority Scheduling
High priority job arrived
High Priority Task
Low Priority Task
Time

## Slide 38: Preemptive Fixed Priority Scheduling
Preempts low priority job
High Priority Task
Low Priority Task
Time

## Slide 39: Preemptive Fixed Priority Scheduling
Lower priority job resumes later
High Priority Task
Low Priority Task
Time

## Slide 40: Preemptive Fixed Priority Scheduling
High Priority Task
Low Priority Task
Time

## Slide 41: Preemptive Fixed Priority Scheduling
High Priority Task
Low Priority Task
Time

## Slide 42: User Mode vs. Kernel Mode
What happens if a task disables interrupts in a pre-emptive OS?
  e.g., EA=0
  Can the OS still force the task to relinquish the CPU?
Clearly, the interrupt switches (and many other things, of course) should only be alterable by the OS only rather than the tasks
  CPU hardware enforces that only the OS can alter them

## Slide 43: User Mode vs. Kernel Mode
How can CPU hardware distinguish OS from other tasks?
  CPU is designed to be in the kernel mode after a reset
  First piece of code running on the CPU should be the OS
  OS always direct interrupts to itself
  Kernel mode flag is set upon interrupts
  OS clears the kernel mode flag before it schedules a task
Q: Does 8051 support user/kernel mode?
  8051 does not have the user/kernel mode design

## Slide 44: Real-Time OS
OS helps to time-multiplex tasks
Some applications need time-related guarantees
  Audio/Video player
  Automotive computer
  Flight control
  Weapon control
  Medical equipment
  Nuclear power plant controller
Q: Are Windows and Linux real-time OS?
  They are not
  e.g., user may experience “正為您更新作業系統… 5%”

## Slide 45: Real-Time OS
Some embedded OSes are designed to offer real-time guarantees
  RTLinux, FreeRTOS, etc.
Real-time levels
  Hard real-time
    Violating time guarantees is not acceptable
  Soft real-time
    Occasionally violating time guarantees is acceptable e.g., video player

## Slide 46: Mutex and Semaphore
Both are synchronization mechanisms among tasks
Handle situation that multiple tasks share a limited number of resources, e.g., UART
  Without synchronization, UART outputs from two tasks may mixed together because of time sharing
Is the following implementation correct?
void task1()
{
while(busy==true);
busy = true;
uartput(“1”);
uartput(“2”);
uartput(“3”);
return;
}
void task2()
{
while(busy==true);
busy = true;
uartput(“A”);
uartput(“B”);
uartput(“C”);
return;
}
bool busy = false;
int main()
{
...
taskCreate(task1);
taskCreate(task2);
taskStartScheduler();
while(1);
}